## Slide 1
Balancing & Control of Segway Robot Using Classical and Modern Control Techniques
(In Submission for Midsemester Research Project Evaluation)
Presented by :
Pritam Ranjan Kalita
MTech Robotics Engineering (3rd Semester)
School of Advanced Engineering
Project Supervisor:
Dr. Rahul Singhal
Electrical Cluster
School of Advanced Engineering

## Slide 2
Figure 1. A self-balancing Segway robot. Adapted from "Self-Balancing Robot Using Arduino" by My Tech Studio, Instructables. Retrieved from https://www.instructables.com/Self-Balancing-Robot-Using-Arduino/. Copyright by Instructables.
Motivation
The Self Balancing Segway Robot is inspired from the Cart & Inverted Pendulum (CIP) model which is a classical problem studied in Control Engineering. The operational principles of CIP model also used in designing of self-balancing hoverboards, Humanoid and Bipedal Robots, Rocket and Missile Guidance systems etc.
Segway-type robots serve as a platform for testing innovative control strategies that can be then extended to more complex robotic systems and autonomous vehicles.

## Slide 3
Literature Review
[1] Mudeng et al. mathematically modeled and simulated a two-wheeled balancing robot, employing a PID controller and Ziegler–Nichol’s method for tuning the PID gains in Simulink.
[2] Putra et al. developed and implemented an LQR-based control system for a two-wheeled self-balancing robot, validating their mathematical model through both simulation and physical experiments.
[3] Mohammed and Abdulla designed an LQR controller to stabilize a Segway robot, and used genetic algorithm and bacteria foraging optimization to tune controller’s Q and R parameters.
[4] Feriyonika and Hidayat in their study implemented Linear Quadratic Gaussian (LQG) control for a two-wheeled self-balancing robot, combining a Kalman filter with Linear Quadratic Regulator (LQR) to reduce sensor noise and optimize balance performance.
[5] Burkan and Ozguney in their study developed and applied adaptive-robust and fuzzy logic controllers for balancing a two-wheeled Segway robot.

## Slide 4
Research Objectives
Study the mathematical model of the Segway Self-Balancing Robot and derive the Transfer function and State-Space model equations for application in design of linear controllers – PID and LQR.
Implement a PID controller for controlling the system. Simulate the results using MATLAB & SIMULINK.
Implement a LQR controller for controlling the system and use Genetic Algorithm for tunning of the Q and R parameters. Simulate the results using MATLAB & SIMULINK.
Implement an advanced Non-Linear Controller for controlling the system. Simulate the results using MATLAB & SIMULINK.

## Slide 5
Methodology
Model Specifications :
Figure 2. Model of the Self-Balancing Segway Robot as simulated in MATLAB-Simulink
Mass of each plate (kg) | 1
Dimensions of each plate (cm) | 18 x 8 x 0.3
Mass of each corner support rod (kg) | 0.0625
Radius of each corner support rod (mm) | 5
Height of each corner support rod (cm) | 25
Dimensions of connecting rod between the wheels (cm) | 20 x 1 x 1
Mass of connecting rod between the wheels (kg) | 0.1
Radius of each wheel (m) | 0.0325
Mass of each wheel (kg) | 0.05
Table 1. Some Model Specifications of the Segway Robot as simulated in MATLAB-Simulink

## Slide 6
Methodology
Mathematical Model of Segway Robot:
Figure 3. Simplified Model of the Self-Balancing Segway Robot used for Mathematical Analysis
Source: [4] Feriyonika, F. & Hidayat, A. (2020). Balancing Control of Two-Wheeled Robot by Using Linear Quadratic Gaussian (LQG).
θ
COM
X
Y
Lc
From our model specifications (last slide), we set some constants which we will need later for finding the Transfer Function and State Space Model equations of the robot :
Mc = Mass of Chassis = 1 kg
Mw = Mass of each Wheel = 0.1 kg
Lc = Distance of COM of the chassis from the axis of rotation of wheels
= 0.129 m
Rw = Radius of each wheel = 0.0325 m
Ic = Moment of Inertia of Chassis rotating abt. Wheel axis
=
Iw = Moment of Inertia of Wheel rotating abt. Wheel axis
=

## Slide 7
Methodology
Mathematical Model of Segway Robot:
Figure 4. Simplified Model of the Self-Balancing Segway Robot used for Mathematical Analysis
Source: [4] Feriyonika, F. & Hidayat, A. (2020). Balancing Control of Two-Wheeled Robot by Using Linear Quadratic Gaussian (LQG).
θ
COM
X
Y
Lc
Non-Linearized Model Equations:
+
Linearized Model Equations:
Assumptions:
;
0
+

## Slide 8
Methodology
Mathematical Model of Segway Robot:
Figure 3. Simplified Model of the Self-Balancing Segway Robot used for Mathematical Analysis
Source: [4] Feriyonika, F. & Hidayat, A. (2020). Balancing Control of Two-Wheeled Robot by Using Linear Quadratic Gaussian (LQG).
θc
COM
X
Y
Lc
Transfer Function of the Segway Robot Plant:
= Chassis Tilt Angle Plant Output (Feedback)
= Torque applied to each individual wheel Plant Input (Control Signal)

## Slide 9
Methodology
Mathematical Model of Segway Robot:
Figure 3. Simplified Model of the Self-Balancing Segway Robot used for Mathematical Analysis
Source: [4] Feriyonika, F. & Hidayat, A. (2020). Balancing Control of Two-Wheeled Robot by Using Linear Quadratic Gaussian (LQG).
θc
COM
X
Y
Lc
State-Space Model of the Segway Robot Plant:
-- State Equation
-- Output Equation

## Slide 10
Methodology
PID Controller Implementation
Plant
(Physical Model / Transfer Function)
PID Controller
Control Signal
(Wheel Torque)
+
-
Feedback (Chassis Tilt Angle)

## Slide 11
Methodology
PID Controller Implementation: Tuning of PID Gains
Mc = Mass of Chassis = 1 kg
Mw = Mass of each Wheel = 0.1 kg
Lc = Distance of COM of the chassis from the axis of rotation of wheels
= 0.129 m
Rw = Radius of each wheel = 0.0325 m
Ic = Moment of Inertia of Chassis rotating abt. Wheel axis
=
Iw = Moment of Inertia of Wheel rotating abt. Wheel axis
=
Transfer Function of the Segway Robot Plant:
= Chassis Tilt Angle
= Torque applied to each individual wheel
MATLAB Code For Getting Tuned PID Parameters:

## Slide 12
Methodology
PID Controller Implementation: Tuning of PID Gains
Code For Getting Tuned PID Parameters:

## Slide 13
Methodology
PID Controller Implementation: Simulink Block Diagram of PID Controller
Figure 4. Block Diagram of PID Controller as implemented in Simulink

## Slide 14
Methodology
PID Controller Implementation: Simulink Block Diagram of Complete Project

## Slide 15
Results
Figure 5: Chassis Tilt Angle () v/s Time Graph from PID Controlled Segway Robot Simulation in MATLAB-SIMULINK

## Slide 16
Results
Figure 5: Control Action/Torque () v/s Time Graph from PID Controlled Segway Robot Simulation in MATLAB-SIMULINK

## Slide 17
Results
Video: PID Controlled Segway Robot Simulation in MATLAB-SIMULINK

## Slide 18
References
Mudeng, V., Hassanah, B., Priyanto, Y. T. K., & Saputra, O. (2020). Design and simulation of two-wheeled balancing mobile robot with PID controller. International Journal of Sustainable Transportation Technology, 3(1), 12-19.
Putra, L. G. B., Wahab, F., & Tamba, T. A. (2025). Design and implementation of linear quadratic regulator control for two-wheeled self-balancing robot. Bulletin of Electrical Engineering and Informatics, 14(2), 931-939.* https://doi.org/10.11591/eei.v14i2.8689
Mohammed, I. K., & Abdulla, A. I. (2020). Balancing a Segway robot using LQR controller based on genetic and bacteria foraging optimization algorithms. TELKOMNIKA Telecommunication, Computing, Electronics and Control, 18(5), 2642-2653.* https://doi.org/10.12928/telkomnika.v18i5.14717
Feriyonika, F., & Hidayat, A. (2020). Balancing control of two-wheeled robot by using linear quadratic Gaussian (LQG). Journal of Telecommunication, Electronic and Computer Engineering, 12(3), 55-61.
Burkan, R., & Ozguney, O. (2017). Balance control of Segway robots using adaptive-robust controller. International Scientific Journal Industry 4.0, 2(1), 38-41.

## Slide 19
Thank You